## Slide 1: Real-time clock-based data logging subsystem in a 5 DOF robotic arm system
Tál Dominik (RHNFAE) – MI MSc.
Lecturer: Dr. Magyar Attila

## Slide 2: Task description
A data logging subsystem shall be designed and developed for the Arbotix-M robocontroller
Logfiles have to be stored on a microSD card
At least 100ms resolution
Choose the proper hardware elements, design the data structure

## Slide 3: Data logging in real-time systems
The ability of the data logger system is that it can collect data in real-time after the logging subsystem is activated, then it will log all the information needed during the monitoring period.
What is data logging?
  Process of collecting and recording data from sensor outputs automatically
Logger element is needed
  LVC125A chip based microSD card adaptor
Must NOT disturb the observed system’s behaviour

## Slide 4: System plan
Realtime clock module (DS1302)
Arbotix-M
Robocontroller
MicroSD shield
Servos
ISP BUS
TTL Dynamixel 3 pin
Serial

## Slide 5: requirements
System design and development has been driven by requirements
I have defined two types of requirements:
  System requirements
  Software requirements
System requirements contain hardware description and some mid level criteria
Software requirements contain the description of SW functionalities and some non-functional details, e.g: Arduino IDE version

## Slide 6: Hardware implementation
Arbotix-M Robocontroller has exactly the same input and output pins as and Arduino Uno microcontroller
Pins used by the DS1302 module (left hand side is the microcontroller side):
  Digital pin 2: RST
  Digital pin 3: DAT
  Digital pin 4: CLK
Pins used by the microSD card shield:
  Digital pin 10: CS
  Digital pin 11: MOSI
  Digital pin 12: MISO
  Digital pin 13: SCK

## Slide 7: Used hardware elements

## Slide 8: Logfile structure
Timestamp needed but DS1302 has only seconds resolution
  Solution is to log the loop count since the latest hard reset  Millis() function
Voltage of the battery is monitored and logged
Servo positions one by one
.csv files are saved to the microSD card
  They can be easily processed later and data visualisation is much more easier

## Slide 9: Software implementation
Component based development
DS1302 and the microSD shield ave their own basic functions
  High level implementation was needed using the given functions
RTC module: time and date setting, time and date reading
microSD shield: secure file opening and closing, folder handling, reading from file and writing to file

## Slide 10: Summary
Good base has been created for the upcoming thesis
Learnt two important and new devices not just for Arduino
It was challenging to develop from a scratch, write the requirements and implement it
Testing documentation has not been created as planned but unit tests have been executed

## Slide 11: Future plans
With the help of the logging funtion a new movement replay function will be developed into the software
A learning function is planned too when the servos release themselves and the user can record a series of movement by positioning the robotic arm manually
Useful for industrial uses – much easier to record operations
Useful for medical uses – rehabilitation exercies could be recorded and taught to patients
Thank you for your attention!